## Slide 1: Directional dark matter search with nuclear emulsions
Valeri Tioukov
INFN Napoli
NEWSdm collaboration

## Slide 2
NEWSdm COLLABORATION
https://arxiv.org/pdf/1604.04199.pdf
81 physicists
23 Institutes
news-dm.lngs.infn.it
ITALY
LNGS,
INFN: Napoli, Roma, Padova
Univ.: Napoli, Roma, Padova,
Potenza, Benevento
JAPAN
Chiba, Nagoya, Toho
TURKEY
METU Ankara
SOUTH KOREA
Gyeongsang University
RUSSIA
LPI RAS Moscow
JINR Dubna
SINP MSU Moscow
INR Moscow
NUST MISiS Moscow
NRU HSE Moscow
Website:
Letter of intent:

## Slide 3: NEWSdm experiment concept
Underground laboratory
Gran Sasso (LNGS)
exposure using telescope
Super-high resolution device
Direction sensitive dark matter search with nano-tracking technologies for super resolution nuclear emulsion
Super resolution detector
Dark matter wind
< 1μm
Tracking
Optical image readout
Unique possibility to overcome the “neutrino floor”, where coherent neutrino scattering creates an irreducible background
Directional information is helpful in understanding the DM model
Notes: 蓄積したデバイス→ 事象解析

## Slide 4
Nano Imaging Tracker (NIT) developed for NEWSdm
electron-
Ag core
Developing
500 nm
AgBr(I) crystal
Density : 3.1 ± 0.1 g/cm3
Crystal size : 20÷80 nm (tunable)
C ions 100 KeV (SEM image)
NIM A Nucl. Inst. Meth. A 718 (2013) 519-521
PTEP (2017)063H01
4
Solid-state detector
Density: 3.1 g/cm3
High-speed volume analysis for nanometric tracks is required

## Slide 5
Optical images with 8 polarizations
L = 213 nm
L = 260 nm
BS = 37nm
L = 200 nm
Alexandrov, A., et al. Super-resolution high-speed optical microscopy for fully automated readout of metallic nanoparticles and nanostructures. Sci Rep 10, 18773 (2020). https://doi.org/10.1038/s41598-020-75883-z
LSPR-based super-resolution imaging based on join deconvolution set of 8 polarized images
SEM
SEM
Super-resolution image
Optical images with 8 polarizations
Super-resolution image

## Slide 6: Joint Image Deconvolution - Comparison with SEM
Angular resolution: 270 ± 30 mrad
Length accuracy: 12 ± 1 nm
Spatial resolution: ~ 60 nm
NIT granularity: 71 nm
Angular distribution
Angular difference
Length difference
SR length vs SEM length
https://doi.org/10.48550/arXiv.2304.03645
Submitted to Sci. Rep.

## Slide 7: Experimental Activity @ Gran Sasso Lab (ITALY)
LNGS surface Lab
Neutron flux @ surface Lab
LNGS underground Lab
Emulsion Handling Facility – Hall F
Production Room Clean Room ISO 6 Capability ~100 g /day
Development Room
Clean Room ISO 7
Jan. 2021 – to date
~1.1 kg of dry NIT produced
>75 developments done
Lead shield : 5.6 cm Polyethilene : 31.5 cm
Target insertion by crane
Shielded Exposure set-up – Hall C
Cooling Box for Target

## Slide 9
Neutron bg study at LNGS (external and underground)
first sub-MeV energy & direction n-spectrum measurement
5.3 mm
（0.5 MeV）
Data:
p recoil tracks - precise energy and direction definition
NIT calibration @ n-beam
MC
E vs range
Beam calibration result

## Slide 10
g-ray (b-ray)
Clearly distinguishable
There is no background in sub-MeV region (2 ~ 14 mm  0.25 ~ 1 MeV in proton energy)
MeV region can be analyzed excluding single-a (especially 210Po peak around 24mm)
Exposed 5x107 g-ray/cm2 from 241Am
(5 years accumulation of environmental g-ray)
Topological or Range cut
50mm
NIT as a Neutron Detector
a-ray
Th star (228Th  208Pb)
5 mm
5.3 mm
（0.5 MeV）
Recoil proton signal
Environmental g-rays cannot become background
5 mm
210Po (24.5mm)
50μm
228Th
220Rn
216Po
212Bi
224Ra
Single-a in U series
T. Shiraishi, et al., Phys. Rev. C 107, 014608 (2023) Environmental sub-MeV neutron measurement at the Gran Sasso surface laboratory with a super-fine-grained nuclear emulsion detector

## Slide 11
PRIN project in medical physics has started in January 2024
100 nanometer resolution required
LNGS hall F: unique in the world underground emulsion production laboratory

## Slide 12
Feasibility test with NIT emulsion detector
7 um grate
10 KeV positron beam
Period is easily visible and measurable
Next step is a real interferometric exposure
NIT samples was produced, developed and analyzed at LNGS

## Slide 13
Muon radiography with nuclear emulsions
Stromboli
La Palma
Vesuvius
Napoli underground Necropolis

## Slide 14
Muon Radiography with nuclear emulsions
A full cycle of emulsion handling and powerful scanning facility, already available in the laboratory, gives LNGS the potential to play a key role in Muography projects based on this technique
Published: 03 April 2023

## Slide 15
THANK YOU FOR ATTENTION!