## Slide 1
Daniel Levin3
Yan Benhamou1
Erez Etzion1
Yiftah Silver1,2
Gilad Mizrachi1
Igor Zolkin1
1 Tel Aviv University
2 Rafael Systems
3 University of Michigan
Muon Radiography
in The Holy Land™
City of David- Wadi Hilweh
In collaboration with
Yuval Gadot4
Oded Lipschits4
Yiftah Sahlev5
4Department of Archaeology & Ancient Near Eastern Cultures, Tel-Aviv University
5Israel Antiquities Authority

## Slide 2
Radiography enables search for subterranean features in sites of antiquity
  sites = tels, city ramparts, burial sites, edifices: pyramids, necropolis
  features = voids, chambers, water conduits, cisterns
  Inexpensive - requires less time, $, manpower than excavation
  Compliments traditional excavation
  Non-invasive  for use in sensitive or inaccessible environments

## Slide 3
New South Wales, Australia
  E. P. George  Measurement of rock overburden of a tunnel
  Technology: Geiger counter. No imaging!
Egypt: 2nd Pyramid of Chephren
  L. Alvarez “Search for Hidden Chambers in the Pyramids,”
  Science 167, 832 (1970)
  Technology: Spark chamber
1989 Laquila, Italy MACRO experiment
  Radiographic evaluation of the rock overburden was a common feature of analyses
2011 The Mu-Ray Project: Imaging of Vesuvius
  Image volcanic summit from the side.
  Technology: hodoscope using extruded plastic scintillators. (adopted from D0)
2023 “Precise characterization of a corridor-shaped structure in Khufu’s Pyramid by observation of cosmic-ray muons”
Nature Comm, March 2023
Muon Radiography/Tomography
200 m

## Slide 4
Muon Radiography/Tomography
“Hidden chamber discovery in the underground Hellenistic necropolis of Neapolis by muography”, Nature April 2023
“Precise characterization of a corridor-shaped structure in Khufu’s Pyramid by observation of cosmic-ray muons”
Nature Comm, March 2023
Current: University of Virginia (E. C. Dukes) Deploy detector pairs at varying locations over two years for 3D imaging.
plus many applications in mining, reactor evaluation, cargo inspection, defense (tunnel searches) etc.
Our interest is in archaeological sites in Israel

## Slide 5
Archaeological tels contain strata of successive civilizations
Tel Hazor
Ancient Canaanite to Israeli city-state
Water systems
תל חצור

## Slide 6
Archaeological tels contain strata of successive civilizations
Tel Azeka
Early bronze to byzantine
David v Goliath
Water systems
Hideouts (Bar Kokhba revolt)
April, 2025 a three-year-old Israeli toddler stumbled upon a 3,800 year old Canaanite seal near Tel Azeka
תל עזקה

## Slide 7
40 cm
40 cm
3.2 cm
4 planes ( 2X & 2Y) interleaved triangular scintillator bars
23 triangular bars/layer x 3.2 x 1.7 cm2
Detector Technology: Extruded Plastic Scintillator
from the FNAL Extrusion Facility
polystyrene + 1% PPO + 0.03% POPOP with TiO2 coating
wavelength shifting fiber (Saint-Gobain BCF-91A)

## Slide 8
Fibers coupled to Hamamatsu S13361-3050 8x8 SiPM array
DAQ: CAEN’s DT5550W platform
== > 4 x 32 channels Citiroc ASICs
Each ASIC is self-triggering
Xilinx XC7K160T FPGA reads out the ASICs and ADCs
3 mm
Readout & DAQ

## Slide 9
Assembled detector in Tel Aviv University Lab

## Slide 10
∆Z = 40 cm
tan𝛉 = ∆x/∆Z
Angular resolution measured: 𝛅𝛉 < ~ 10 mrad
∆X
Muon Tracking
Hit position: charge weighted avg:
Xavg = (Qi*Xi +Qi+1 * Xi+1)/(Qi+Qi+1)

## Slide 11
Detector Staging in
The City of David / Wadi Hilweh
City of David regarded as Jerusalem 1.0 ==> established by King David 1000 BCE
Objective: search for signs of passages to Gihon Spring, the city’s water source
All ancient cities needed a water supply and fortified,
secret ways to get to there in case of emergency or war*
* Prof. Oded Lipschits, director of Ancient Israel Studies at the Tel Aviv University

## Slide 12
via Dolorosa
Holy Sepulcher
Gethsemane
Dome of the Rock
Western Wall
Al Aqsa Mosque
Muon Detector
nachal qidron
Kidron

## Slide 14
Attempting to install at Warren’s Shaft
10th century BCE access to the Gihon Spring

## Slide 15
First operational test: Placement in “Jeremiah’s” Cistern
arxiv 2504.03078

## Slide 16
Down a steep stairs past
Warren’s Shaft
Placed inside a cave

## Slide 17
define angular bins:
Extract the count rate Ru per angular bin
Generate the “expected“ angular count rate distribution in GEANT4 ==> look for anomalies
or
3) Normalize to the acceptance to get the muon flux Fu
& extract the eff overburden from rate vs depth relation
Measurement method

## Slide 18
Simulated example of void detection
-
=
2 x 1 x 1 m air void 4 m above the detector.
The surrounding volume is rock.

## Slide 19
Modeling in GEANT4 Basic elements
Detector (idealized – fully efficiency, resolution)
Muon generator  Ecomug.h
“EcoMug: An Efficient COsmic MUon Generator for cosmic-ray muon applications”
NIM A Volume 1014, 21 October 2021. D. Pagano, G. Bonomi, A. Donzella, A. Zenoni, G. Zumerle, N. Zurlo
Terrain:
 topographic arrays created using GoogleEarth Pro, ArcGIS Pro, VisualizeGPS
 represented in GEANT4 as a lego construction with 2 x 2 m grid

## Slide 20
Al Aqsa
Dung Gate
detector
Building a GEANT4 Model
include terrain of Jerualem’s Old City: Temple Mount, Al Aqsa, the Western Wall
Givati excavation

## Slide 21
GEANT4

## Slide 22
Open Sky Hit Distribution
Detector #1 in Tel Aviv Lab
▲Detector Data
◼︎GEANT4

## Slide 23
Time between events
Slope give rate  0.23 Hz
Preliminary Site Data

## Slide 24
Preliminary Site Data vs MC
Early data quality are “good”
Cave environment features:
Dirty – soil, dust, rock debris
High humidity
Rocky platform
Low BW connection
Low security
Difficult access
Some channels required repairs
Gain required optimization
Detector in
City of David
GEANT4
GEANT4
Detector in
City of David
Detector #2 in Jerusalem Cave

## Slide 25
Data
Preliminary Site Data vs MC
GEANT4

## Slide 26
Summary & Next steps
Pilot detector installed and operational.
New detector deployment in Jerusalem in Sept.
A new major grant proposal underway with Archaeological, Physics & AI
Identification of sites with archeological potential & detector accessibility
  eg: tel Azeka has network of known tunnels for calibration and unknown conduits
  Deployment of multiple detectors with intersecting / overlapping FoV
  May use boreholes for subterranean placement
  Use NN pattern recognition to achieve true 3D tomography

## Slide 27
backup

## Slide 28
Hz
1.0
0.1
0.01
0.001
0.0001
0.1 1.0 10 100 1000 GeV
Integrated track rate for Detector #2 in Jerusalem
rock at 260
at 200
at 120
What is sensitivity at Silwan site?
Integrate dN/dE E > Emin Emin depends on zenith angle, path thru rock

## Slide 29
Elevation profile at detector location
max rate at 460 elev
Detector normal: 260 elev
200 elev

## Slide 30
Elev Angle | distance [m] | Emin [GeV] | track rate [Hz] | Tracks/month full acceptance | tracks thru test feature | Differential
46 | 8 | 4.6 | 0.25 | 648K | 550K -- 980K | 300K
26 | 20 | 10.8 | 0.11 | 285K | 5K –6K | 1000
20 | 50 | 27 | 0.037 | 96K | 700 | 70
Total detector rate at 260 = 0.23 Hz
Example rates assume:
  uniform density calcite rock (2.7 g/cm3)
  acceptance is independent of energy, orientation
  90% hit efficiency  64% track efficiency
  Test feature = 3 x 3 x 3 m3
  1 month data

## Slide 31
Dome of the Rock
Al Aqsa Mosque
Muon Detector Kidron
Matson (G. Eric and Edith) Photograph Collection
Library of Congress: LC-DIG-matpc-05871
(Date unknown, but consistent with late 19th century)