## Slide 1
FDS Lessons Learnt: LIGO
Begüm Kabagöz, Vicky Xu, MIT FDS Team, LIGO FDS Team, LIGO Instrument Team
2025-10-20
Next Generation Collaborative Design - Frequency-dependent Squeezing

## Slide 2: Outline
Alignment on HAM7 table very stable
Alignment from HAM7  HAM5 stable, except big shifts happened twice
Optical System Overview
Control System Overview
FC Design and Real Life
FC and Arm Power
FC Backscatter
Squeezing and Thermal Effects
Smaller Problems

## Slide 3: Optical System Overview – HAM7 & HAM5
Squeezer + Filter Cavity
ZM4 R4(V)
ZM3
ZM5 R5(V)
ZM2 R2(V)
ZM1
FC1 R=1m
FC2
to ZM6 OFI SRM OMC
VOPO
SQZ Generator
q Controller Alignment
Alignment q Controller
q Controller
Freq. dep. phase rotator
Alignment on HAM7 table very stable
Alignment from HAM7  HAM5 stable, except big shifts happened twice: LLO76905, LLO68097
LIGO DCC G2502387

## Slide 4: Optical System Overview – Vacuum Injection Platform
﻿﻿T1900649 FDS final optical layout
5 total passes through Faraday Isolators
1% loss if well aligned (LLO62852)
Tight space on on the platform, easy to clip the beam.
5 - 8.5 dB injection loss plausible
LLO62811
LIGO DCC G2502387

## Slide 5: Optical System Overview – HAM7 & HAM5
﻿﻿T1900649 FDS final optical layout
LIGO DCC G2502387

## Slide 6: Optical System Overview – Full IFO
Source Table
Detection Table
To IFO
Fibers from source table for green OPO pump, green FC, IR auxiliary beams CLF&RLF
Free-space path to detection table

## Slide 7: Control System Overview
W. Jia, A+ O4 Squeezing Layout G2301114
ADF Loop
LIGO DCC G2502387

## Slide 8: Control System Overview
Squeezer Laser – Main Laser
Frequency Lock (SQZ TTFSS)
Pre-Mode Cleaner Lock (SQZ PMC)
SHG Cavity Lock (SQZ SHG)
OPO Lock with Green Pump Beam (Green + IR co-resonance)
Coherent Locking Field (CLF) Phase Lock to OPO (CLF2f Loop)
OPO Green & CLF Intensity Stabilization ON
FC Lock with Green
(feedback to Green frequency & to FC length)
Detune FC until Resonant Locking Field (RLF) near resonance
Switch the FC length control from Green error signal to IR error signal (beat between RLF and CLF @105 kHz)
SQZ TTFSS second path error signal CLF-IFO beat at OMC trans (LO Loop)
Switch the SQZ phase control from CLF2f to Audio Diagnostic Field
Activate FC IR alignment loops
Frequent FC Green lock loss
Green-IR frequency noise
Sensitive to GR alignment
LIGO DCC G2502387
Notes: During hand-off stage, error signal uses half of ADCs range. Easy to rail with high ground motion.

## Slide 9: FC parameters design vs current
FC & related parameters | Design (T1800447) | Current
Arm power | 750-800 kW | 270-300 kW
CTN | 0.5 x CTNaLIGO | CTNaLIGO
IFO  FC light and backscatter to IFO | 50 pW (DC readout) 90 dB isolation 20 dB below DARM | <20 dB below DARM @ 10 Hz ~10 dB below DARM 100-300 Hz
FC Length | 300 m | ~300 m
FC Ti (input coupler T) | 1100-1200 ppm | 800-1000 ppm
FC round trip loss | 60 ppm | 40-100 ppm
FC linewidth | 2 * 45 Hz | 74 Hz
FC & related parameters | Design (T1800447) | Current
Arm power | 750-800 kW | 270-300 kW
CTN | 0.5 x CTNaLIGO | CTNaLIGO
IFO  FC light and backscatter to IFO | 50 pW (DC readout) 90 dB isolation 20 dB below DARM | <20 dB below DARM @ 10 Hz ~10 dB below DARM 100-300 Hz
FC Length | 300 m | ~300 m
FC Ti (input coupler T) | 1100-1200 ppm | 800-1000 ppm
FC round trip loss | 60 ppm | 40-100 ppm
FC linewidth |  | 74 Hz
LIGO DCC G2502387
Notes: OFI thruput 99.3 % alog 55716
Fc cavity length noise req
deltaL/L = deltaf/f
<1.5 urad

## Slide 10: Squeezing at Parm =280 kW suffers misrotation
begum@mit.edu
GWINC SuperQK branch
Using math from L. McCuller, et al. Phys. Rev. D 104, 062006 (2021)
T2500310 - A+/O5 strain curve projections
T2500348 – A+/O5 quantum noise projections
Misrotation <50 Hz
Pointed out also in W. Jia et al. Science 385,1318(2024)
LIGO DCC G2502387

## Slide 11: FC parameters are more suitable for squeezing with Parm =550 kW
begum@mit.edu
FC-IFO dephasing becomes limiting
Related to Ti, Lrt, injected squeezing
T2500310 - A+/O5 strain curve projections, T2500348 – A+/O5 quantum noise projections
LIGO DCC G2502387

## Slide 12: Squeezing with higher Parm highly dependent on CTN
begum@mit.edu
BNS range calculated for Quantum Noise.
Parameters optimized for each arm power and CTN. CTN defined as factor * aLIGO CTN
aLIGO CTN (Gras, G200088)
T2500310 - A+/O5 strain curve projections, T2500348 – A+/O5 quantum noise projections
T1800447 - FDS Design Reqs evaluates this too.
LIGO DCC G2502387

## Slide 13: FC backscatter with 2 SQZ Faraday Isolators (+ OFI)
LLO 72088
T1800447 - FDS Design Requirements
FC backscatter is isolated enough with 2 SFIs.
Potential issues with backscatter at LHO86836, upstream of SFI2
Peaks come from sensing, but don’t show up on DARM during injections. Need additional work on this projection.
LIGO DCC G2502387
Notes: FC linewidth requirement is tied to the pondermotive squeezing we want to pre-compensate for. So this of course means, we either need a very long FC or very high finesse.
High finesse means more stringent requirements on IFO backscatter from FC. FC backscatter noise depends on the fc length noise ofc. And BHD vs DC readout has a difference.
The design is estimated to have <20 dB below darm. Highly alignment dependent and temp needs optimizing.
Lower finesse means we can live with higher Tin & rtloss
FC IR finesse :500kHz/75 Hz ~6700
FC GR finesse:

## Slide 14: SQZ and IFO Thermalization
begum@mit.edu
During IFO thermalization (assuming TCS works as intended):
X – Y arm mode mismatch changes (technical noise)
Squeezing angle rotates (we fix with ADF servo, LLO75568, LLO75807)
Squeezer – IFO mode mismatch changes
Signal Extraction Cavity detuning changes
IFO – SEC – Output Mode Cleaner mismatch changes
K. Kuns and D. Brown, P2500132: “Squeezed state degradations due to mode mismatch and thermal aberrations in gravitational wave detectors”
LIGO DCC G2502387
Notes: ADF: Audio diagnostic field

## Slide 15: High freq. noise affects measurable squeezing
LLO78418
V. Frolov
Arm mode mismatch to each other
Input jitter coupling to dark port
Measurable squeezing level degradation at 2 kHz
Ultimately, we can look at other bands for squeezing level diagnostics. More importantly: technical noise trumps shot noise.
LIGO DCC G2502387

## Slide 16: SQZ and the Static Thermal State of IFO
Thermal state of the test masses affects IFO beam, AND SQZ-IFO mode matching.
We scan SQZ beam parameter using PSAMs when needed. LLO72594: discussion on PSAM scans for power levels. LLO75184: ring heater related scan.
PSAM curvature control is coupled to PSAM alignment. Srivastava et al. Opt. Express 30, 10491 (2022) talks about the tilt in phase front.
Mode matching scan becomes very time consuming.
LHO Power down decision G2301151 (low freq. noise + lock stability)
We need better sensing and control over thermal state of the test masses.
SQZ beam can be used as a probe for IFO beam in full lock, if we have wavefront sensing for SQZ beam.
LIGO DCC G2502387
Notes: ADF: Audio diagnostic field

## Slide 17: Squeezing needs robust Thermal Control
CO2 alignment shift
Jul 2: Beckhoff restart
Jul 9: Power glitch
May 8-9: Computer outage & Power glitch
PS: PSAM scan
CO2 down
ABW: Auto beam walk
CO2 misaligned on CP
recovery
High power experiments
PS
PS
ABW
ABW
PS
Xtal move
LIGO DCC G2502387

## Slide 18: Misalignment can degrade low frequency noise too
Inferred change, LLO72729
SQZ-IFO mismatch | 5 %, 1 rad | 1 %, 0.4 rad | 
 | Alignment A |  | Alignment B
18
Right now we have no working SQZ-IFO alignment servo. Error signal (AS42) offset changes.
We align SQZ-IFO when needed, using ZM4/6 beam walking.
LIGO DCC G2502387
Notes: Few percent mismatch. This can easily happen due to misalignment and/or mismatch. We already have indications that misalignment can add to lf noise.

## Slide 19: Mode matching losses in SQZ Loss Budget
19
Credit: V. Xu
Mode matching is a big part of total loss.
Mode matching phases can destructively/constructively interfere <400 Hz.
We have to think of squeezer with the rest of the IFO.
L. McCuller, et al. Phys. Rev. D 104, 062006 (2021)
Phase noise 20-30 mrad
LIGO DCC G2502387

## Slide 20: Small(er) Problems that need solving
20
OPO crystal degradation
We move crystal position ~every 10 months, to a new spot. We will need new crystals soon.
After crystal move, rapid degradation
  To keep same nonlinear gain, we increase green power to OPO cavity.
  Input power to pump fiber increases, risky.
  (Solved issue: must adjust crystal temperature (auto: LLO77278) and sqz phase angle changes (ADF servo).)
Green power level issues
LHO SHG output power variations cause FC green locking threshold issues
Polarization rotation through the pump fiber causes increase in input power to the pump fiber, risky.
FC green-IR frequency noise
Filter cavity commissioning without IFO beam was problematic. May be due to fiber delivery.
  Fiber phase noise cancellation schemes?
  Making alternative locking paths available would be nice. (e.g. FC Green error TTFSS)
FC bounce modes ring up with proportional gain on length control servo
LIGO DCC G2502387

## Slide 21: O4 FDS Performance at LLO
O4a: First run with FDS. Starts strong at ~-5.8 dB, degrades over time to ~-5 dB.
O4b: Starts at ~-5.8 dB, degrades with TCS events, recovered to ~-6 dB, maintained there. Large spread in the histogram. Big progress in understanding the behavior and how to improve.
O4c: ~-6 dB before the break, ~-5.5 dB after. Operated with lower input power, higher absorption in the arms. Thermal state changes and test mass beam spot moves mean many cycles of mode matching and alignment optimization needed. Excellent uptime performance, robust control achieved, small variance in histogram.
Squeezing Level: May 24th 2023 - Aug 31st 2025
Figure credit: A. Mulavey, also used in G2501943
Uptime = FDS time/Observing time*100
O4a (2023/05/24 – 2024/01/16): 99.4%
O4b (2024/04/10 – 2025/01/28): 95.3%
O4c (2025/01/28 – 2025/03/11): 100%
LIGO DCC G2502387

## Slide 22: Conclusion
Alignment on HAM7 table very stable
Alignment from HAM7  HAM5 stable, except big shifts happened twice
Many FC locking failures due to GR-IR frequency noise
Optimal FC parameters are arm power dependent and CTN dependent
Squeezing is highly dependent on thermal state
Squeezer misalignment can can couple noise to DARM<100 Hz
We have to think about the squeezer in the context of the full system
BHD – SQZ interaction is unknown right now
Dr. Begüm Kabagöz, MIT Kavli Institute, LIGO Labs
LIGO DCC G2502387

## Slide 24: Loss, Phase noise and Squeezing Level
NLG determines the generated squeezing. Loss and phase noise compromise the attainable squeezing level.
E. Oelker, et al. Optica 3, 682-685 (2016)
: normalized NL interaction strength
Estimates: 23% losses, 10 mrad phase noise, 19 NLG
LLO alog 73225 73188
Dr. Begüm Kabagöz, MIT Kavli Institute, LIGO Labs
begum@mit.edu